## Slide 1
Autonomous Underwater Lionfish Harvester
Phase III
Background
What are Lionfish?
  Lionfish are an invasive species in the Atlantic
  Lionfish can grow up to 15” and weigh approximately 2.6lbs
  Female lionfish can lay 2,000,000 eggs per year
Why are Lionfish a problem?
  They have no natural predators in the area
  They devastate local fish populations and threaten coral reef habitats
  Lionfish can eat anything up to 2/3 their body size
What is being done to alleviate the issue?
  There are little to no fishing regulations
  Organizations host lionfish hunting derbies
  Countries are promoting Lionfish consumption
Human Limitations on diving
  Scuba diver fisherman are limited to ~130 ft depth
  Lionfish have been spotted as far as 820 ft
Why Autonomous?
  Robotic harvesters that are operated through a tether can damage the coral reefs
  As a result most are not allowed in the areas
Key Objectives
The overall goal of our MQP was to implement an autonomous system to hunt and capture lionfish with the following objectives:
1.) Navigate the AUV’s environment effectively and thoroughly while avoiding obstacles and fragile reef habitats.
2.) Identify lionfish with greater than 90% accuracy and pursue them safely, without alarming them, and with the same intent as objective 1.
3.) Spear and harvest lionfish with a capacity of minimum 5 fish.
4.) Establish basic communications with mothership
System Architecture Overview
Brief Overview
Lionfish are an invasive species in the Caribbean Sea and on the Eastern Coast of the USA.
This MQP proposes a fully autonomous robotic solution to kill and capture the invasive species.
Building off previous teams’ work, this year’s focus is on developing a new harvesting system, refined identification algorithm, and autonomous navigation algorithm.
Identifying Lionfish and Divers
17,000 Images for Training
  14,000 Lionfish
  5,000 Divers
SSD MobilenetV2 performed the best
References
“Red Lionfish | National Geographic.” [Online]. Available: https://www.nationalgeographic.com/animals/fish/r/red-lionfish/. [Accessed: 03-May-2020].
“1985-2018 Lionfish Invasion.” [Online]. Available: https://www.usgs.gov/media/images/1985-2018-lionfish-invasion. [Accessed: 02-May-2020].
“lionfish (Pterois volitans/miles) - Species Profile.” [Online]. Available: https://nas.er.usgs.gov/queries/FactSheet.aspx?speciesID=963. [Accessed: 03-May-2020].
Michael Abadjiev (RBE/ME) | Leo Chen (RBE/ECE) | Clark Ewen (ECE) | Nicholas Johnson (RBE/CS),
Nicholas Olgado (ECE) | Harrison Saperstein (RBE) | Orion Strickland (RBE/ME) | Christopher Whimpenny (CS/ME)
Advisors: Prof. Craig Putnam (RBE/CS) | Bradley Miller (RBE) | Prof. William Michalson (RBE/ECE/ME)
Chart: NNs Recall vs. FPS Performance
| 20.626097320579571 | 17.19566759359704 | 7.5067898832254629
 | 0.7552 | 0.72984 | 0.48405
Acoustic Link – Wireless Communications
Communication between robot and boat.
  Vital for disarm, return home
  Protocol with CRC frame for error proof.
  Symmetrical design in hardware and protocol
Signals are carried by sound wave through the water.
Piezo transducer to transmit and receive sound waves.
On-off keying used to modulate the signals.
Demodulation done by microcontroller through sampling and edge detection.
SSD MobilenetV2: Actual
SSD MobilenetV2: Ground Truth
The system was developed on the BlueROV2 underwater rover system.
3 separate computing devices were added to the system:
  Jetson Nano – for running the identification neural network and making high-level navigation and emergency decisions.
  Arduino Mega – for integrating and managing different sensors and the spear mechanism.
  ARM Board – for processing communications with the topside boat.
Chamber 1 includes the existing BlueROV2 infrastructure, connected to our added components in chamber 2 via an IP network configuration.
Convolutional Neural Networks (CNN)
  1.) SSD MobilenetV2
    FPS: 20.6
    Recall: 0.76
  2.) SSD InceptionV2
    FPS: 17.2
    Recall: 0.73
  3.) SSD Resnet
    FPS: 7.5
    Recall: 0.48
Navigation
The navigation system was created using motion building blocks:
  Move Forward/Backward
  Ascend/Descend
  Turn to a heading
Using sonar, we implemented object detection to navigate safely.
Combining the building blocks and obstacle detection, we were able to create more advanced search patterns.
The AUV’s mission flowchart for navigating an
Ocean environment.
Harvester Mechanism
Pneumatics powered spear Spin-Spear rotating mechanism One motor to flip and store Lionfish Container
- No elastic bands, no springs - One fluid motion to flip and store - Single DC motor - One-way fish valve
- Vent into evacuated exhaust chamber - Rack and pinion flippers - quick-swap AUV attachment