## Slide 1: Center for Imaging and Sensing (CIS)
Raunak Borwankar, Ian Costanzo, Gene Bogdanov, Sasidhar Tadanki, Reinhold Ludwig
ECE Department
Worcester Polytechnic Institute
100 Institute Road
Worcester, MA 01609
Phone: 508-831-5231
October 10, 2017

## Slide 2: Center Organization
Objective
  To assist our industrial partners in their quality assurance and imaging requirements
What we deliver
  Inspection and imaging methodologies
  Fundamental sensor and instrumentation research
  Turn-key prototype system development
  Circuit design, simulations, layouts
Organization
  Two full-time ECE faculty
  Funded graduate research assistants
  ECE software/hardware tools, shop resources

## Slide 3: Approach
Regular meetings with our partners
  Company-specific research updates
  Demonstration of prototypes
  Presentations by undergraduate/graduate project students
Use of industry standard tools
  HFSS, ADS, Matlab, SolidWorks, etc.
Dissemination of research
  Research reports
  Conference/journal publications
  Student theses

## Slide 4: 1st Example: Electrical Impedance Tomography (EIT) of Polycrystalline Diamond Cutters
Problem description
  Have to characterize cutter performance nondestructively
  Need to detect hidden defects in a cost-effective way
Approach
  Measure electrical conductivity
    Diamond table conductivity depends on residual metal content
    Metal content is correlated with cutter performance characteristics
  Localized conductivity measurement can detect defects (metal-rich zones, cracks)
Tungsten Carbide Substrate
Polycrystalline Diamond
PDC Bit

## Slide 5: EIT System Development
What we built
  EIT data acquisition system
    Sensor with 120+2 pogo pins
    Analog front end (custom PCB)
    Pneumatic system for placing cutter in contact with the sensor
    Machine vision system for diamond table thickness measurement
  Custom-developed 3D EIT software
    FEM forward solver
    GPU-accelerated iterative inverse solver
Outcomes
  Two machines in industrial use for more than 5 years
  Conductivity dataset acquired and reconstructed in 5 sec
  1 journal paper, 3 conference papers
  1 patent granted
~3000 measurements
Conductivity reconstruction is a nonlinear
inverse problem with ~3000 unknowns

## Slide 6: 2nd Example: Machine Vision System for Diamond Thickness Measurement
Problem description
  Diamond cutter EIT requires diamond thickness for quantitative conductivity measurements
What we built
  Machine vision system using specular reflection contrast
  Cutter is rotated by an existing roller system
  Full rotation is detected by image correlation
  Blur radius measurement for focusing
Outcome
  One prototype in use and coupled to one of the EIT machines

## Slide 7: 3rd Example: High-Pressure Gasket Moisture Content Measurement
Problem description
  Soft material is used as a gasket and pressure transmission medium
  Excess moisture gasket can cause failure during decompression
    Potential catastrophic damage to press anvils
  Need a nondestructive method of monitoring gasket moisture content
Approach
  Electric RF field/moisture interaction
Pressure cell assembly
Pyrophyllite
Cube (gasket)
Steel
Current Ring
Salt Bushing
Heater Assembly
Metal Disc

## Slide 8: High-Pressure Gasket Moisture System
What we built
  Coaxial resonator sensor
  Sample loader
  Rapid moisture content estimation software
  Experimental multimode cavity sensor
Outcomes
  5 moisture meters installed at our industrial partner
  3 QNDE papers
  1 patent application filed
experimental
sensor

## Slide 9: 4th Example: Electrochemical Leaching of Polycrystalline Diamond
Problem description
  Metal must be removed from polycrystalline diamond to a certain depth to meet performance specifications
  Existing process using HF-HNO3 mix is slow, inconsistent, prone to yield issues, and dangerous
  Our partner needs a replacement process
Approach
  Electrochemical metal removal
  Amount of metal is related to accumulated charge
  Nontoxic chemicals
Voltage
Source
(-) electrode
(+) electrode
e-
Co2+
Citric Acid
HEAT
Masking

## Slide 10: Electrochemical Leaching System
What we built
  Multichannel (48-channel) potentiostat
    Applies voltage to cells
    Measures current in each leaching cell
    Accumulates charge
    Stops current when reaching calculated charge level
    Ethernet connectivity
  Central control software for large number of potentiostats
  Individual cutter cells (jointly developed)
  Oven for heating cells (jointly developed)
Outcomes
  6 potentiostat prototypes deployed (24, 32 and 48-channel versions)
  Large amount of data collected
  1 patent application filed

## Slide 11: 5th Example: Lock-in Thermography for Bearing Braze Joint Inspection
Problem description
  Bearings for well drilling use polycrystalline diamond
  Diamond-tipped inserts are brazed into the bearing body
  Poor braze joints cause premature failure
  Need a nondestructive braze joint inspection
Approach
  Low braze joint area results in weak thermal contact with the body
  Measure thermal conduction from inserts to the body via lock-in thermography

## Slide 12: Bearing Braze Joint Inspection System
What we built
  Lock-in thermography system
    Heating by 1000 W halogen lamp
    Sinusoidal modulation of lamp output
    IR camera images surface temperature evolution over time
  Software to compute phase shift between heat source and temperature
    Robust measure of thermal diffusivity
Outcomes
  1 prototype constructed
  Successfully detected 1 bad braze joint in a limited number of samples

## Slide 13: 6th Example: Bore Inspection
Problem description
  Need to detect surface-breaking pores with resolution of 100µm in diameter on bore wall
Approach
  Machine vision
  Specular reflection contrast
    Bore wall strongly reflective
    Pores less reflective
  Fast, low cost
    No sophisticated part manipulation (e.g. rotation-translation)

## Slide 14: Bore Inspection System
What we built
  Imaging system
    High-resolution 5 MP camera
    Wide angle, short standoff lens
    Ring light illumination
  Sample loader
  Image processing software
    Bore wall unwrapping
    Defect detection
Outcomes
  Simulated pores detected on wide-bore (0.452”) parts
    Parts modified: rough bore bottom
  Revision is under development to improve contrast
    Axial illumination
Camera
Lens
Ring light
Sample
xyz stages
Slide
unwrapped bore

## Slide 15: 7th Example: Magnetic Resonance Imaging Dual-Tuned Head Coil
Problem description
  Demand for dual-tuned clinical MRI transmit/receive head coils for sodium (23Na) and hydrogen (1H) at 3T for stroke imaging
  Wide frequency separation between 23Na at 34 MHz and 1H at 128 MHz
    Higher frequency circuits inhibit the performance at the lower frequency, which is most critical
Approach
  Experimental coil design
    Birdcage at low frequency (34 MHz)
    TEM-like coil at high frequency (128 MHz)

## Slide 16: MRI Dual-Tuned Head Coil
What we built
  Simulated competing coil designs
    Experimental birdcage-TEM coil
    Typical dual-tuned birdcage coil
    Dual-tuned TEM coil
  Built and tested a prototype birdcage-TEM coil
Outcomes
  NIH SBIR grant awarded
  Prototype performed similarly to simulation
B1 field with load:
top – 34 MHz (23Na)
bottom – 128 MHz (1H)

## Slide 17: 8th Example: Solid-state 2 kW 2.45 GHz Microwave Generator
Problem description
  Semiconductor industry looking to replace magnetron MW generators with solid-state versions
    More controllable and reliable
  Challenges
    small package (4U rackmount)
    waveguide output
    efficient, pulsing capable
    low cost, short development time
Approach
  Combine outputs of eight 330 W solid-state power amplifier modules

## Slide 18: Solid-state Microwave Generator
What we did
  Designed output stage with custom MW components:
    power combiners
    power dividers
    directional couplers
    waveguide transition
  Tested 2-way combined 330 W modules
Outcomes
  2-way prototype performed well
    up to 550 W output
    no oscillation
    pulsing capable
custom 2-way combiner
8-way output
stage layout
2-way combined prototype